## Slide 1
1

## Slide 2: CONTENTS
*
2
Introduction
Design Specifications
DAC Theory
Design Procedure
Result
Conclusion & Future works

## Slide 3
3
1. Introduction
Data converter is found in applications ranging from high-end computing systems to smart mobile devices
DAC and ADC is the main part of data converter
DAC convert the digital code input to analog output to connect to the real world
• Applications:
• Storage media
• Audio
• Mobile phone
• Routers

## Slide 4
4
State of the art DAC
P. Caragiulo, C. Daigle, and B. Murmann, DAC Performance Survey 1996-2020,” [Online]. Available: https://github.com/pietro-caragiulo/survey-DAC
Higher Power, Higher Speed
Higher speed, lower SFDR

## Slide 5
5
State of the art DAC
 | [20] | [21] | [6] | [22]
Year | 1999 | 2006 | 2010 | 2021
Technology | 0.5µm | 180nm | 65nm | 7nm
Resolution | 12 | 10 | 12 | 8
Power Dissipation (mW) | 140 | 216 | 188 | 308
Sampling Rate (MSPS) | 200 | 250 | 2,900 | 97,000
SFDR (dB) | 70 | 62.3 | 56 | 40.76
[6]C. -H. Lin et al., "A 12 bit 2.9 GS/s DAC With IM3 ≪− 60 dBc Beyond 1 GHz in 65 nm CMOS," in IEEE Journal of Solid-State Circuits, vol. 44, no. 12, pp. 3285-3293, Dec. 2009.
[20] A. Van den Bosch et al., "A 12 bit 200 MHz low glitch CMOS D/A converter," Proceedings of the IEEE 1998 Custom Integrated Circuits Conference (Cat. No.98CH36143), Santa Clara, CA, USA, 1998.
[21] J. Deveugele and M. Steyaert, "A 10b 250MS/s binary-weighted current-steering DAC," 2004 IEEE International Solid-State Circuits Conference (IEEE Cat. No.04CH37519), San Francisco, CA, USA, 2004.
[22] R. L. Nguyen et al., "8.6 A Highly Reconfigurable 40-97GS/s DAC and ADC with 40GHz AFE Bandwidth and Sub-35fJ/conv-step for 400Gb/s Coherent Optical Applications in 7nm FinFET," 2021 IEEE International Solid-State Circuits Conference (ISSCC), San Francisco, CA, USA, 2021.

## Slide 6
6
Trending DAC topologies
[2] G. Manganaro, Advance Data Converters. Cambridge University Press, 2012.

## Slide 7
7
2. Design Specifications
DESIGN PARAMETERS |  | SPECIFICATIONS
VDD |  | 1.2V
Technology |  | 65nm
Resolution |  | 12
Fsamp |  | 500MS/s
SFDR |  | 70dB@250MHz
ENOB |  | 11
Power |  | 60mW
PVT | Process | 5 case of MOS
 | Temperature | -20˚C to 125˚C

## Slide 8
8
3. DAC Theory
N is the total number of bits of the digital word

## Slide 9
9
Binary weighted and Thermometer Current Steering DAC
Feature | Binary-Weighted DAC | Thermometer-Coded DAC
Complexity | Simple | Need decoder
Monotonicity | Not guaranteed | Guaranteed
Glitches at Mid-Code | Severe | Minimal
Best Use Case | Low-precision (<8-bit) | High-precision (> 8 bits)
Matching and glitch problems of a binary-weighted DAC.
Matching and glitch advantages of a thermometer-coded DAC.
[12] Chi-Hung Lin and K. Bult, "A 10-b, 500-MSample/s CMOS DAC in 0.6 mm/sup 2/," in IEEE Journal of Solid-State Circuits, vol. 33, no. 12, pp. 1948-1958, Dec. 1998
binary-weighted
Thermometer

## Slide 10
10
Segmentation current steering
Comprehensive overview of the specifications of unary, binary, and segmented implementations.
Normalized required area versus percentage of segmentation.
[12] Chi-Hung Lin and K. Bult, "A 10-b, 500-MSample/s CMOS DAC in 0.6 mm/sup 2/," in IEEE Journal of Solid-State Circuits, vol. 33, no. 12, pp. 1948-1958, Dec. 1998
[15] A. van den Bosch, M. A. F. Borremans, M. S. J. Steyaert and W. Sansen, "A 10-bit 1-GSample/s Nyquist current-steering CMOS D/A converter," in IEEE Journal of Solid-State Circuits, vol. 36, no. 3, pp. 315-324, March 2001

## Slide 11
4. Design Procedure – DAC Implementation
11

## Slide 12
12
Thermometer Encoder

## Slide 13
13
Thermometer Encoder – Schematic and Layout

## Slide 14
14
Local Decoder
Used to check whether the previous cell is turned on.
If so, the next cell is enabled

## Slide 15
15
Latch
The latch synchronizes input signals, ensuring all switches in the current cell activate at the same time.

## Slide 16
16
Current cell issue
Current cell with switch signal transition
=> Use driver to level-shift switch signals instead of just aligning timing

## Slide 17
17
Driver - Schematic
The output voltage work from 0 to 0.6V
= 100uA * 6kΩ=600mV

## Slide 18
18
Current Cell – Design
Basic Cell
Cascode current source Cell
More output impedance
Better ENOB
Lower glitch
Lower output swing
MP1
MP3
MP2

## Slide 19
19
Current Cell Design – Final result
W = 400n
L = 1u
Biasing Circuit
Cascode switch
W = 10u
L = 2u
W = 5.2u
L = 400n
W = 150n
L = 60n
W = 150n
L = 60n
Cascode current source

## Slide 20
Full circuit
Binary to thermo Decoder
Current Biasing
Binary weighted cell
Thermometer cell
Dummy Decoder

## Slide 21
Layout - Floorplanning

## Slide 22
Layout – Current source arrays

## Slide 23
Layout – Full DAC
Area: 1.84 x 1.3 mm2

## Slide 24
5. Result - Testbench
Ramp Signal

## Slide 25
Static Performance
Using ramp signal to ADC to find DNL and INL

## Slide 26
INL Result
Worst-case INL = 0.5LSB

## Slide 27
DNL Result
Worst-case DNL = 0.6LSB

## Slide 28
Dynamic Result
1024 samples, fin = 249.5MHz, Fsamp = 500MHz, include 4G noise transient

## Slide 29
Comparison current cell
Cascode current source cell
Cascode current source and cascode switch cell
Cascode current source cell
Cascode current source and cascode switch cell
=> Use cascode switch to minimize glitch, increase ENOB

## Slide 30
Spectrum Result
Spectrum with 249.5 MHz signal with and 500 MHz clock

## Slide 31
PVT result

## Slide 32
PVT result
 | Min | Max | Typical | Post sim @TT | Post sim @100MSPS
Power Dissipation (mW) | 32.47 | 47.12 | 40 | 47.3 | 37.16
DNL (LSB) | 0.3 | 0.6 | 0.5 | - | -
INL (LSB) | 0.2 | 0.5 | 0.4 | - | -
SFDR (dB) | 68.72 | 85 | 83.5 | 30.7 | 67.4
ENOB | 10.6 | 11.8 | 11.8 | 4.56 | 10.17

## Slide 33
Comparison
 | [6] | [11] | [19] | This Work
Technology | 65nm | 65nm | 90nm | 65nm
Resolution | 12 | 12 | 12 | 12
Power Dissipation (mW) | 188 | 30 | 128 | 40
DNL (LSB) | 0.3 | 0.23 | 0.5 | 0.6
INL (LSB) | 0.5 | 0.4 | 1.2 | 0.4
Update Rate (MS/s) | 2900 | 300 | 1250 | 500
SFDR (dB) | > 66 | 75.98 | 66 | 83.5
Bandwidth (MHz) | 300 | 30 | 625 | 250
ENOB | 10.67 | - | 10.67 | 11.8

## Slide 34
Conclusion & Future work
Project Overview: Designed a 12-bit DAC 500MSPS in 65nm CMOS.
Achieved 11.8-bit ENOB at 500 MSPS (schematic), and 10.17-bit at 100 MSPS (post-layout).
Low power consumption: 41mW total.
High linearity: DNL = 0.6 LSB, INL = 0.5 LSB.
Robust across PVT corners.
Applied techniques:
                + Cascode current source
                + Cascode switch.
                + 3 to 7 bits binary to thermometer decoder.
Future Work
Layout optimization to improve post-layout performance → tape-out ready.
Add digital calibration (e.g., DEM) for higher accuracy and speed.
Explore system-level integration:
→ Use in optical transceivers for high-speed data center applications.

## Slide 35
35
THANK YOU

## Slide 36
Reference
[2] G. Manganaro, Advance Data Converters. Cambridge University Press, 2012..
[4] P. Caragiulo, C. Daigle, and B. Murmann, DAC Performance Survey 1996-2020,” [Online]. Available: https://github.com/pietro-caragiulo/survey-DAC.
[6] C. -H. Lin et al., "A 12 bit 2.9 GS/s DAC With IM3 ≪− 60 dBc Beyond 1 GHz in 65 nm CMOS," in IEEE Journal of Solid-State Circuits, vol. 44, no. 12, pp. 3285-3293, Dec. 2009.
[11] G. M. Hong, Shih-Hsuan Hsu, Yan-Hua Peng, Alvin Hsin-Hung Chen, Yi-Ti Wang and Hsin-Hung Lu, "A 10-bit 300MHz 0.1mm2 triple-channel current-steering DAC 75.98dB SFDR in 65nm," 2008 IEEE International Symposium on VLSI Design, Automation and Test (VLSI-DAT), Hsinchu, 2008.
[19] Wei-Hsin Tseng, Chi-Wei Fan, and Jieh-Tsorng Wu. A 12-bit 1.25-gs/s dac in 90 nm cmos with 70 db sfdr up to 500 mhz. Solid-State Circuits, IEEE Journal of, 46(12):2845–2856, 2011.
[20] A. Van den Bosch et al., "A 12 bit 200 MHz low glitch CMOS D/A converter," Proceedings of the IEEE 1998 Custom Integrated Circuits Conference (Cat. No.98CH36143), Santa Clara, CA, USA, 1998.
[21] J. Deveugele and M. Steyaert, "A 10b 250MS/s binary-weighted current-steering DAC," 2004 IEEE International Solid-State Circuits Conference (IEEE Cat. No.04CH37519), San Francisco, CA, USA, 2004.
[22] R. L. Nguyen et al., "8.6 A Highly Reconfigurable 40-97GS/s DAC and ADC with 40GHz AFE Bandwidth and Sub-35fJ/conv-step for 400Gb/s Coherent Optical Applications in 7nm FinFET," 2021 IEEE International Solid-State Circuits Conference (ISSCC), San Francisco, CA, USA, 2021.

## Slide 37
37
Static Characteristics of DACs
Differential nonlinearity (DNL) is a measure of the separation between adjacent levels measured at each vertical jump
Integral Nonlinearity (INL) is deviation of actual output from ideal output across full range
Monotonicity: A DAC is monotonic if output never decreases with increasing input.
Monotonicity Guaranteed if

## Slide 38
38
Dynamic Characteristics of DACs
Dynamic performances of a DAC (a) Time domain response
(b) Frequency domain measure
Time Domain Characteristics:
  • Settling Time: Time to stabilize output after a step input.
  • Glitch: Spurious spikes due to code transitions.
  • Clock Feedthrough: Capacitive coupling of clock signals to output.
Frequency Domain Characteristics:
  • SNR: Signal-to-noise ratio like the quantization noise and the noise produced by the components in the circuit, excluding harmonics.
  • SFDR: Ratio of signal power to highest spur.
  • ENOB: Effective resolution based on SNR or SFDR.

## Slide 39
39
DAC architectures

## Slide 40
Application DAC
A. Khairi et al., "Beyond 200-Gb/s PAM4 ADC and DAC-Based Transceiver for Wireline and Linear Optics Applications," in IEEE Open Journal of the Solid-State Circuits Society, vol. 4, pp. 265-276, 2024,

## Slide 41
41
Current Cell – Current source design
To calculate the sizing for cell better, we need to know the and , this parameters depend on technology, and we will use monte carlo to find it. Monte Carlo simulations are carried out for 100 runs each for various WL values

## Slide 42
42
Current Cell – Current source design
The values for Avt and Ab are estimated to be 3.3mVm and 10% m

## Slide 43
43
Current Cell – Current source design
In order to maintain an INL 0.5 LSB, is defined as
Where C = inv norm(0.5 yield/2). To maintain a high yield, the value of C was chosen to equal 3
%
Choosing Vov = 0.2V, so (W/L) = 4
=> L 14.32um, W = 57.28um

## Slide 44
44
Current Source Design – Output impedance
The current cell output resistance influences the INL by approximately
INL =
The required current cell output impedance for a given SFDR is
For this design, with 70 dB SFDR, 12 bit and 25Ω load resistance the minimum required current cell output resistance is calculated to be 100 MΩ.

## Slide 45
45
Current Steering DAC
Current Steering architecture with two types of implementation a) The Binary Implementation and b) The Unary Implementation.
Current Steering DAC
Generates output current by summing contributions from active current sources.
Current is steered to output nodes—not just switched off—to maintain stable biasing.
Supports binary, unary, or segmented input coding
Output Configurations
Single-ended: Used in low-frequency/control systems.
Differential: Preferred in modern systems for better noise immunity and distortion suppression.
Key Features
Output impedance = parallel of active current cells.
Differential outputs cancel even-order harmonics and reduce common-mode noise.
Compact area, high-speed operation.
a)
b)

## Slide 46
46
Thermometer Encoder – Schematic Cadence
Wp = 600nm
FingerP = 8
Wn = 200n
FingerN = 8
Wp = 600nm
FingerP = 8
Wn = 200n
FingerN = 8
Wp = 600nm
FingerP = 10
Wn = 200n
FingerN = 10
Wp = 600nm
FingerP = 18
Wn = 200n
FingerN = 18
Wp = 600nm
FingerP = 8
Wn = 200n
FingerN = 8
Wp = 600nm
FingerP = 2
Wn = 200n
FingerN = 2
Wp = 600nm
FingerP = 6
Wn = 200n
FingerN = 6
Wp = 600nm
FingerP = 4
Wn = 200n
FingerN = 4
Wp = 600nm
FingerP = 10
Wn = 200n
FingerN = 10
Wp = 600nm
FingerP = 10
Wn = 200n
FingerN = 10
Wp = 600nm
FingerP = 10
Wn = 200n
FingerN = 10

## Slide 47
47
Thermometer Encoder - Result
A
T1
B
C
T1
T2
T3
T4
T6
T5
T7

## Slide 48
48
Local Decoder
Wp = 600nm
FingerP = 8
Wn = 200n
FingerN = 8
Wp = 600nm
FingerP = 8
Wn = 200n
FingerN = 8
Wp = 600nm
FingerP = 16
Wn = 200n
FingerN = 16
Wp = 600nm
FingerP = 16
Wn = 200n
FingerN = 16

## Slide 49
49
Local Decoder - Testbench
VDD, VSS
Input B2T

## Slide 50
50
Local Decoder - Result
ROW
COL
PRE ROW
OUTN
OUTP

## Slide 51
51
Latch – Schematic
Wp = 200nm
FingerP = 10
Wn = 200n
FingerN = 10
Wn = 200n
FingerN = 6
Wp = 200nm
FingerP = 4
Wn = 200n
FingerN = 2
Wp = 200nm
FingerP = 1
Wn = 200n
FingerN = 1
Wp = 200nm
FingerP = 1
Wn = 200n
FingerN = 1
Wn = 200n
FingerN = 8

## Slide 52
52
Latch – Result
OUTN local decoder
OUTP local decoder
CLK
OUTN latch
OUTP latch

## Slide 53
53
Driver – Result
INN
INP
OUTP
OUTN

## Slide 54
Result – Post simulation

## Slide 55
Result – Post simulation @100MSPS

## Slide 56
General system of Optical communication system – DSP based

## Slide 57
Appendix
A 2 GS/s 14-bit current-steering DAC in 65 nm CMOS technology for wireless transmitter
A 12 bit 2.9 GS/s DAC With IM3 < - 60 dBc
Beyond 1 GHz in 65 nm CMOS

## Slide 58
Appendix
Voltage scaling DAC
This DAC uses 2N equal resistors to divide the reference voltage into 2N levels. Digital input controls switches to select one of these voltage levels as output. The output voltage is given by:
It is simple and monotonic but not practical for high resolutions (N > 8) due to large area and delay.
An output buffer is needed to drive the load and reduce distortion at high frequencies.
Resistor String DAC

## Slide 59
Appendix
Binary weighted resistor and R-2R resistor ladder – Current scaling
Binary weighted resistor DAC architecture
R-2R resistor ladder DAC architecture
Binary weighted resistor
Uses N resistors weighted by bit significance
Analog output is the sum of bit-controlled currents.
Requires low output impedance, so a buffer/amplifier is used for accurate current-to-voltage conversion.
Sensitive to resistor matching, especially for high-bit resolutions.
R-2R Ladder DAC
Uses only two resistor values: R and 2R, simplifying layout and improving matching.
Offers smaller area, better accuracy, and lower power than binary-weighted DACs.
Sensitive to switch resistance mismatch, limiting resolution.
Bandwidth of output buffer often limits speed → best for low-cost, low-resolution applications.

## Slide 60
Appendix
Capacitor DAC
Uses capacitors instead of resistors to generate analog output.
If all capacitors are equal, input is encoded in thermometer code; for binary input, binary-weighted capacitors are used.
Active bits switch their capacitors from GND to Vref, and output voltage is set by total charge redistribution.
Advantage: No continuous current flow → low power consumption.
Resilient to timing jitter: total charge stays constant despite small delays.
Main limitation: Capacitor mismatch causes non-linearity.
Common in pipeline ADCs and SAR ADCs.